# ENGINEERING ADVISORY NOTE				EAN 02

## Erection of Regulatory Speed Limit Signs

Roads ACT has completed a review of the existing regulatory speed limit signs in the ACT and currently undertaken a project to rectify deficiencies and non compliance with the relevant standards.

As part of this project all regulatory speed limit signs currently associated with other signs (composite) will be erected on a standalone post.  In order to reinforce this concept in the Asset Acceptance future projects, the following advice is provided.

Advice:

- All regulatory speed limit signs should be erected on a standalone post except the School Zone sign and the speed limit signs associated with temporary traffic management.

- If an electric pole (EP) is located at a particular location, it could be considered to erect a regulatory speed limit sign if all other requirements are met and no other signs exist on the pole.

- Gated speed limit signs should not be erected on undivided roads. If gated signs are necessary to enforce speed limits or other safety reasons, the sign on the right should be erected on a median island. In the case of roads with inadequate width to install a median island, other options such as repeater signs or larger signs should be considered with prior approval.

## Administrative Arrangement

This technical direction takes effect from date of endorsement by the Director.

Prepared by:						Scrutinised by:

Lingam Jatheendran					Gabriel Joseph

Chief Engineer					Senior Manager

Asset Acceptance					Asset Acceptance

27 September 2012					27 September 2012

Authorised by:					Authorised by:

David Roulston					Tony Gill

Director Operational Support				Director Roads ACT

Territory and Municipal Services			Territory and Municipal Services

Date:							Date: